PRESENTATION ON WORK PROCESS AT LW FABRICATION SHOP
RAKESH M
BE MECHANICAL
UNDER THE GUIDANCE OF,
MOHANKRISHNA(DGM)
LW FABRICATION SHOP
BEML KGF COMPLEX

---
LW FABRICATION
BE 1OOO (REVOLVING FRAME,DECK LH&RH)
BE 700(REVOLVING FRAME,DECK)
BD 30W(REAR CHASSIS)
14 TH(REAR CHASSIS)

---
FABRICATION
FABRICATION IS THE PROCESS OF BUILDING METAL STRUCTURES BY CUTTING,BENDING AND ASSEMBLING PROCESS.
ASSEMBLING PROCESS IS CARRIED OUT AT LW FABRICATION SHOP , CUTTING AND BENDING PROCESS AT PLATE SHOP.
ASSEMBLING CAN BE DONE BY TWO WAYS
1)TEMPORARY JOINTS.
2)PERMANENT JOINTS.

---
JOINTS DESCRIPTION
TEMPORARY JOINTS
1)USING BOLTS AND NUTS.
PERMANENT JOINTS
1)WELDING.
2)RIVETING.

---
WELDING
- WELDING IS PROCESS OF JOINING ANY TWO MATERIALS USING A THIRD MATERIAL AS BINDER.
- MOST COMMON MATERIAL USED IN INDUSTRIES ARE MILD STEEL WITH DIFFERENT COMPOSITIONS AS PER REQUIREMENT .
- WELD ON THE MATERIAL SURFACE TAKES PLACE BY THE MELTING OF THE BINDER MATERIAL AND NOT THE BASE MATERIALS HENCE IT IS A CONVENIENT FABRICATION PROCESSS

---
TYPES OF WELDING
- GMAW or Gas Metal Arc Welding.
- GTAW or Tungsten Inert Gas.
- Arc Welding or SMAW.
- Gas or Oxy Acetylene Welding And Cutting.
- SAC or Submerged arc Welding

---
WELDING PROCESS AT LW SHOP
GMAW (GAS METAL ARC WELDING)
IN THIS PROCESS A SHIELDING GAS CARBON DIOXIDE IS USED
PREVENT CONTAMINATS FROM AIR AND FUSING MATERIAL MS
WIRE WITH COPPER COATING MELTS AND FORMS A LAYER.
SAW(SUBMERGED ARC WELDING)
FLUX IS HEATED TO HIGH TEMPERATURE AND FUSED ON THE LAYER AS A COAT

---
STRUCTURES WELDED AT LW SHOP
- REVOLVING FRAME
- DECK LH&RH
- REAR CHASSIS
- STEERING CASE
- C-FRAME

---
FABRICATION PROCESS
- MATERIAL FROM PLATE SHOP
- FABRICATION FIRST STAGE AND LAYOUT
- MACHINING PROCESS
- FABRICATION FINAL STAGE
- FINAL PAINTING AND QUALITY CHECK
- TO ASSEMBLY

---
THANK YOU